## Slide 1: Bike Lane Maintenance Treatments
Deschutes County Road Department
2016 OACES CHIP SEAL WORKSHOP
December 07, 2016
Chris Doty, Director
Tom Shamberger, Operations Division Manager

## Slide 2: Road Department Mission Statement
  We strive to maintain the quality and improve the experience for all users of the Deschutes County transportation system.

## Slide 3: Cross-section of a Chip Seal
3/8” Coated Chip Seal
1/4” Coated Chip Seal
New Asphalt

## Slide 4: Past trial effort: Use of seal coat in bike lane
Baker Road, SE Bend Area
Carbon Seal®
Bike Lane
3/8” Chip Seal
Travel Lane
FY 11/12
Baker Road/China Hat Rd
Camp Polk Road
FY 12/13
Deschutes Market Road
Knott Road
Butler Market Road
FY 13/14
Old Bend Redmond Highway

## Slide 5: Deschutes County use of seal coat in bike lane
Carbon Seal®
3/8” Chip Seal

## Slide 6: Current Bike Lane Maintenance Practices
  1. Install smaller chip rock (1/4” minus) on all facilities with designated bike lanes (or where we can achieve width with lane narrowing on high use cycling routes).
  2. Reduce lane width to 11’ (from 12’+) on all striped facilities (unless high truck volume or existing 5-foot bike lane)

## Slide 7: Johnson Road Treatment

## Slide 8
TRAVEL LANE CHIP SEAL
BIKE LANE CHIP SEAL
EXISTING ASPHALT

## Slide 9
Johnson Road Lane Treatment
with ¼” - #10 chip rock.
3/8-#8
¼-#10

## Slide 10: 1/4” - #10 bike lane chip adjacent to 3/8” - #8 travel lane chip
Cline Falls Road: pre chip seal
12’ travel lanes, 3’ shoulder
Cline Falls Road: post chip seal
3/8” chip travel lane
1/4” chip bike lane
11’ travel lanes, 4’ bike lane
3/8-#8
¼-#10

## Slide 11: 1/4” - #10 bike lane chip adjacent to 3/8” - #8 travel lane chip
  Northwest Way
3/8” chip travel lane
1/4” chip bike lane
11’ travel lanes, 3’ shoulder
River Summit
3/8” chip travel lane
1/4” chip bike lane
11’ travel lanes, 4’ bike lane
¼-#10

## Slide 12
Pre Lane Width Adjustment
Powell Butte Highway
Post Lane Width Adjustment
Powell Butte Highway

## Slide 13
Pre Lane Width Adjustment
Lower Bridge Road
Post Lane Width Adjustment
Lower Bridge Road

## Slide 14
Use of small steel roller in
Bike Lanes

## Slide 15: Feedback on County Roads and Chip Seals
Via email: “I rode my bike on the chip seal that you guys did west of Shevlin Park. It was pretty nice. I think it was the smoothest chip seal I have ever ridden on.”
Public tweet:

## Slide 16: Questions

## Slide 17: DOUBLE CHIP SEAL Maintenance Treatments
Deschutes County Road Department
2016 OACES CHIP SEAL WORKSHOP
December 07, 2016
Chris Doty, Director
Tom Shamberger, Operations Division Manager

## Slide 18: Strategic Pavement Investment
Chip seal = $
Overlay = 6 to 8 x $
Full Depth Rec = 15 to 20 x $
Reconstruct = 20 to 40 x $
Chip seal
Chip seal
Chip seal

## Slide 19
Pavement Maintenance Strategy
Arterials – Full depth, overlay or grind and inlay
Collectors – Full depth, overlay or grind and inlay
Local Roads – Chip Seal

## Slide 20
Options for Local Roads
PCI 65 to 80:
Crack Seal
Asphalt Patch
Single Chip Seal
PCI – 45 to 65
Road has good profile
Asphalt patch
Double Chip Seal

## Slide 21
BENEFITS OF DOUBLE CHIP SEAL
Doubles the protection from oxidation and deterioration from moisture
Can be successfully used on moderate to severely deteriorated and cracked roads
Extremely durable and flexible surface which reduces and significantly delays cracking
Improves skid resistance and winter traction due to the textured surface

## Slide 22
Double Chip Seal
3/8 - #8
1/2” – 1/4”

## Slide 23
Double Chip Seal Candidate
PCI of 38

## Slide 24
Second Lift On Double Chip Seal

## Slide 25
½” - ¼” chip seal keyed with 3/8-8

## Slide 26
Double Chip Seal
PCI of 84 two years later

## Slide 27
Wendy Road – La Pine
Road into truck stop
PCI of 20

## Slide 28
First Lift at .52 Gallon / sq. yd.
Cracks filled with oil

## Slide 29
Oil Shot Rate: 1st Lift - .52 gal./sq. yd.
2nd Lift - .41 Gal /sq. yd.
Rock Rate: 1/2” - 1/4” - 25 lbs. / sq. yd.
3/8” - # 8 - 17 lbs. / sq. yd.

## Slide 30
Desert Road

## Slide 31
Severe Rutting not candidate for double chip

## Slide 32
Tom Shamberger, Operations Manager
Deschutes County Road Department
Tom.Shamberger@deschutes.org
(541) 322-7120
Questions