## Slide 1: Tools in the Toolbox 2019 OACES Chip Seal Workshop Kyle Arntson Albina Asphalt
Specialty Emulsion Products

## Slide 2: Specialty Emulsion Products
PMCRS-2H
RS-LTP

## Slide 3: PMCRS-2H
What is it?
Cationic
Rapid setting
Hard penetration based asphalt
Properties
Min. Max.
Viscosity 100 400
Penetration 40 90
Where to use it?
High traffic volume roads
Steeper road grades
Higher temperature zones

## Slide 4: RS-LTP
What is it?
Low temperature oil
Rapid setting
Chemical break
Properties
Min. Max.
Viscosity 50 NA
Breaking index NA 80
Penetration 150 300
Where to use it?
Higher humidity, fog or mist
Heavily shaded environments
Low ambient temperatures

## Slide 5: RS-LTP
Located near river
Higher humidity, fog and misty conditions
Highly canopied
Shady and damp areas
Good rock embedment
Successful embedment with adverse environment and weather conditions

## Slide 6: Additional tool for the Toolbox
Road Resources
  Interactive website
  Designed for selecting the best pavement preservation treatments
  Outlines lifecycle costing for roads
  https://roadresource.org/
  https://roadresource.org/toolbox/criteria