## Slide 1
Chip Seal Prep
Jackson County

## Slide 2
Jackson County – 765 center line miles of surfaced roads
  Much are matt coated with multiple layers of chip seals
2006 - Headed towards a cliff
  Chip seal program = 32 miles
  24 years until the whole system would be chip sealed
  No overlay program
  PCI was tanking
2016 - Pavement condition improving
  Chip seal effort = 72 miles
  10.6 years until the system would be chip sealed
  PCI predicted to be 76 this FY and headed up
  Corresponding increase to chip seal preparation
      - THIS HAS BEEN KEY!
Change in Approach to Pavement Maintenance

## Slide 3
Jackson County
Pavement Condition Index (PCI)
Chart: 
| 05-06 | 06-07 | 07-08 | 08-09 | 09-10 | 10-11 | 11-12 | 12-13 | 13-14 | 14-15 | 15-16 | 16-17
 | 80 | 77 | 75 | 74 | 72 | 70 | 69 | 71 | 72 | 73 | 74 | 76

## Slide 4
Include the Cost of Chip Seal Prep with your Chip Seal Budget
Often the cost of the chip seal is stated as the cost of Chips + Oil
    (w/ labor and equipment already budgeted)
Include prep costs and shorten chip seal list if you cannot do adequate prep
Example: 2016 Season @ 72 CL miles (950K yd2)
 | Tons | Cost | Cost/Mile
½" C-Mix | 12,500 | $637,500 | $8,854
Emulsion | 1,239 | $675,255 | $9,376
Chips | 9,592 | $143,887 | $1,998
Total |  | $1,456,642 | $20,228

## Slide 5
So what would we recommend for chip seal prep?
1. All chip seal prep you do before the chip seal is a good thing – but more is better.
    - Preferably a season ahead of the chip seal
2. Steal every good idea you have ever seen or heard
    - Lane County – Blade Patching
    - ODOT – grind / inlays
3. Be honest in looking at your shortcomings
    - All too often we celebrate how good we are doing when in reality we need to improve
4. Develop “tools” for chip sealing – be creative

## Slide 6
Don’t Chip Seal Junk (w/out fixing it)
Prep Needed:
Medium alligator cracking
Medium to high severity distortions
High severity longitudinal and transverse cracking
High severity failed patches
Medium to high severity rutting

## Slide 10
Chip Seal Prep Tool Box
Using our tool box (along with good drainage), Jackson County typically gets 9-12 years out of a 3/8” chip seal
    Tool Box
    Grind / Inlay Patches
    Blade Patch
    Crack Seal
    Chip Seal “Patches”
    Scrub Seals
    Fog Seals

## Slide 11
Grind / Inlay Patches

## Slide 12
Grind / Inlay Patching
Beg, borrow, rent, contract for or steal a grinder – it will change your program – we love our Wirtgen 100
Steps:
  Remove failed area 2.5” – 4” deep
  Sweep grind - skid steer w/ front broom works best for us
  Tack w/ CSS-1 (we hate our Lee Boy Tack Tank)
  Spread AC w/ chute box by an experienced dump person
  Straddle patch w/ push screed and loader – Adjust as needed
  Rake out edges, highs, lows, sides and ends (raking is critical)
  Roll to finish
  Fix what you missed
  Water the patch

## Slide 16
5 functions: depth, side shift, angle tilt and width adjustment
Being able to pave an edge grind w/o a strong shoulder is golden to us
We do leave loader tracks on the patch so we use slicks

## Slide 19
This needs to be completed in good order or the crew gets spread out

## Slide 20
Blade Patches
Sunken grades
High severity Distortions
High severity rutting and depressions
High severity raveling

## Slide 21
Tack low area
Spread mix
Remove Knife River clods
Lay out mix
Rake off bones
Roll & Water

## Slide 22
Crack Sealing
Graze, pick and blow clean cracks. 1” – 2” deep ¼” or wider
Fill crack with the proper filler with a very thin overband
Detac if picking is evident
As a last resort we mist with a water truck to break surface stick

## Slide 23
Adds more value than often given credit for
Staffing this crew is getting increasing harder

## Slide 24
Chip Seal “Patches”
Fill shallow ruts with one or two layers of chip seal
3/8” -#8 covered by ¼” - #10 and then chipped over

## Slide 25
Scrub Seals / Fog Seals
Scrub Seals
When the road is sound but fully cracked.
Avoiding massive overband fields
Jackson County completed 5 + miles last season
Chipped over the Scrub Seal
Fog Seals
Choking fresh patches with emulsion and sand to prevent chip loss
.10 to .25 (.25 thanks to bad knife river RAP mix)

## Slide 26
Questions
Chip Seal Prep
Jackson County