## Slide 1: Road Pavements are “Supported” Bridges

## Slide 2
Enemies of Roads:
  Water penetration – Freeze / thaw/ expansions / voids
  Traffic Loading
    High Traffic Use (verses low traffic counts)
    Truck Loads – one loaded truck may cause the same amount of damage of 5,000 cars
  Weathering / Seasonal Climate / Age
    Breakdown of aggregate and asphalt oils
      May allow water penetration
      Need Aggregate surface for traction
Most Road Pavements failures are contribute to when the “Support” has been jeopardized

## Slide 3
Enemies of Roads: continued
  Artificial Damage
    Stud Tires
    Utility Cuts
    Traffic Accidents – liquids spilled
    Farm equipment dragging
    Stopping areas = pavement thrusting
    Bus Stops
  Others items that shorten the life of roads
    Poor drainage
    Poor or non-maintained shoulders
    Tree roots
    Inadequate Road Base, Design, Road Materials, Construction practices/ Workmanship, Lack of Good Maintenance, or Neglect

## Slide 4: Typical Distresses
Alligator cracking
Block cracking
Longitudinal & transverse cracking
Delamination
Rutting
Potholes

## Slide 5: Cracking
Alligator

## Slide 6: Cracking

## Slide 8: Localized Failures

## Slide 9: Surface Treatments & Costs
Crack Seal: $4k/mile (3-6 years) {costs greatly vary}
Slurry Seal: $8k/mile (4-6 years) {urban street treatments}
Chip with Fog Seal with prep: $34k/mile (7-12 years)
2” Maintenance AC Overlay: $120k/mile (10-20 years)
Grind & 2” AC Inlay: $150k/mile (12-20 years)
4” Structural AC Overlay: $190/mile (14-20 years)
Reconstruction: $500k/mile (20-24 years)

## Slide 10: Pavement Management Systems
Inventory of road pavements - Section Descriptions
Provides Maintenance & Rehab (M&R) history
Produce a list of upcoming M&R work
Demonstrates current health & performance of roads
Predicts roads’ projected performance and costs
Estimate a required project and system wide budget
Planning/ Maintenance/ Design Construction
Aids in defining what work should be done when

## Slide 11: How PMS Software/ System Works
Segment roads into management units
Visual survey of pavements every 1-4 years
Sample ~10% of roadway surface in each segment
Enter data on various distresses
Using Pavement Condition Index (PCI) of
  100 is new/ perfect road to 0 = Failed road,
  calculate the PCI values
Output = recommended treatments within assigned budgets and many other reports

## Slide 12: Pavement Condition Rating with Typical Repairs
100
90
80
70
60
50
40
30
20
10
5 yrs
10 yrs
15 yrs
20 yrs
PCI
Repair
Cost/Yard
$.80
$1.50
$8
$13
$30 plus
Seal Cracks
Single Chip Seal
Overlay
Thick Overlay
Reconstruct
Good
Fair
Poor
Very Good
Very Poor
Failed
Pay now or pay later
Excellent
0

## Slide 13: Pavement Condition Index PCI
100
85
70
55
40
25
10
0
Excellent
Very Good
Good
Fair
Poor
Very Poor
Failed
Corps of Engrs Develop for Airfields
ASTM now has standards for both highways and airfields
Analyze Distresses
  Type
  Severity
  Density
Adopted by most agencies

## Slide 14: Pavement Condition
Pavement Condition Index
PCI = 88
Time / Traffic Loading
100
0
20 years
10 years
Notes: The difference between the effect of preventive and reactive maintenance is significant. Not only is the timing of application different, but the effect (represented by the slopes of the after-treatment performance curves) is also different.

## Slide 15: Pavement Condition
Critical PCI = 65 - 70
20 years
Pavement Condition Index
Time / Traffic Loading
100
0
10 years
Notes: The difference between the effect of preventive and reactive maintenance is significant. Not only is the timing of application different, but the effect (represented by the slopes of the after-treatment performance curves) is also different.

## Slide 16: Critical PCI
Preventive Maintenance
Corrective Maint, Rehabilitation, or Reconstruction
Critical PCI
Pavement Condition Index
Time / Traffic Loading
100
0
20 years
10 years
Notes: The difference between the effect of preventive and reactive maintenance is significant. Not only is the timing of application different, but the effect (represented by the slopes of the after-treatment performance curves) is also different.

## Slide 17: Ideal PCI
100
0
80
Ideal Management Range
85
Ideal Management Range of PCI of 80 to 85
is accepted by agencies’ pavement managers
as the range or “Industry Standard”
to be the most cost-effective of
maintaining a road network.
This should be the network PCI performance target
Pavement Condition Index
Time / Traffic Loading
20 years
10 years
Notes: The difference between the effect of preventive and reactive maintenance is significant. Not only is the timing of application different, but the effect (represented by the slopes of the after-treatment performance curves) is also different.

## Slide 18: Preventive Maintenance
Preventive
Maintenance
Pavement Condition \ $ Costs
$
Time / Traffic Loading
20 years
10 years
Notes: The difference between the effect of preventive and reactive maintenance is significant. Not only is the timing of application different, but the effect (represented by the slopes of the after-treatment performance curves) is also different.

## Slide 19: Corrective Repairs
Corrective
Maintenance/ Repair
Pavement Condition \ $ Costs
more$
Time / Traffic Loading
20 years
10 years
Notes: The difference between the effect of preventive and reactive maintenance is significant. Not only is the timing of application different, but the effect (represented by the slopes of the after-treatment performance curves) is also different.

## Slide 20: Rehabilitation
Rehabilitation
Pavement Condition
even more$
Time / Traffic Loading
20 years
10 years
Notes: The difference between the effect of preventive and reactive maintenance is significant. Not only is the timing of application different, but the effect (represented by the slopes of the after-treatment performance curves) is also different.

## Slide 21: Reconstruction
Pavement Condition \ $ Costs
Time / Traffic Loading
Reconstruction
most costly$
20 years
10 years
Notes: The difference between the effect of preventive and reactive maintenance is significant. Not only is the timing of application different, but the effect (represented by the slopes of the after-treatment performance curves) is also different.

## Slide 22
100
90
80
70
60
50
40
30
20
10
7 years
14 years
21 years
28 years
Pavement Condition Index PCI
Good
Fair
Poor
Very Good
Very Poor
Failed
Pavement Condition Index with Typical Repairs
0
Excellent
Single Chip Seal $1.50
Seal Cracks $.80
Thin Overlay $8
Thick Overlay $13
Reconstruct $30 plus
Repairs Cost per Yard
New
Pay Now
or Pay Later...
Pavement Deterioration Curve

## Slide 23
Road Condition: Excellent
Treatments: Minimal to None
Service Cost: Minimal to None
Inventory Trend: Severe Decrease
Well Maintained Barn

## Slide 24
Road Condition: Very Good
Treatments: Seals & Patching
Service Cost: $1.50/ sq yd
Inventory Trend: Slight Decrease
Minor Repairs

## Slide 25
Road Condition:
Good to Fair
Treatments: Overlays
Service Cost: $8/ sq yd
Inventory Trend: Severe Increase
Major Repairs

## Slide 26
Road Condition: Poor to Failed
Time to Rebuild!
Treatments:
Generally
Reconstructions
Service Cost:
$30 plus /sq yd
Inventory Trend:
Increase

## Slide 27: An Analogy
Process is continuous and inevitable
The rate of water flow increases as condition decreases
The effort to pump water increases with decreasing condition
Need a bigger ($) pump!
Seal =
$1.50 / sq yd
Overlay =
$8 / sq yd
Reconstruct =
$30 / sq yd

## Slide 29
Maintained vs Non-Maintained County Road
Cost per Mile for 2 Lane Road Over 55 years
Pavement
Condition
Index (PCI)
Maintained
Non-Maintained
Years
The poorer the road, the greater the liability.
0
20
40
60
80
100
0
5
10
15
20
25
30
35
45
55
Rebuild
$300 K
Rebuild
$300 K
Seal
$9 K
Seal
$9 K
Overlay
$91 K
Seal
$9 K
Seal
$9 K
Overlay
$91 K
Seal
$9 K
Seal
$9 K
Maintained
Total =
$236 K
Life Avg.
PCI = 90
Non-Maintained
Total =
$600 K
Life Avg.
PCI = 76
Excellent
Very Good
Fair
Failed
=
=
40
50
Initial Building Cost
$300 K

## Slide 30
Maintained vs Non-Maintained County Road
Average PCI Experienced Over 55 years
Pavement
Condition
Index (PCI)
Maintained
Non-Maintained
Years
50
60
70
80
90
100
0
5
10
15
20
25
30
35
45
55
Maintained
Life Avg.
PCI = 90
Non-Maintained
Life Avg.
PCI = 76
40
50
Rebuild
Rebuild
Overlay
Overlay

## Slide 31
Maintained vs Non-Maintained County Road
Average PCI Experienced per Dollar Spent Over 55 years
Maintained
Non-Maintained
Years
0
5
10
15
20
25
30
35
45
55
Maintained
Life Avg.
BPR = 17.0
Non-Maintained
Life Avg.
BPR = 8.4
40
50
PCI NO$
PCI $
0
5
10
15
20
25
30
35
Rebuild
Rebuild
Overlay
Overlay
Buying
Power
Ratio*
(BPR)
Initial investment ($300 K) is included in calculations
Comparison Ratio = 2.02
* Buying Power Ratio = Avg. PCI Mile / $100,000 Invested

## Slide 32
Maintained vs Non-Maintained County Road
Average PCI Experienced per Dollar Spent Over 55 years
(Inflated at 3% Annually)
Maintained
Non-Maintained
Years
0
5
10
15
20
25
30
35
45
55
Maintained
Life Avg.
BPR = 10.3
Non-Maintained
Life Avg.
BPR = 3.4
40
50
0
5
10
15
20
25
30
35
Buying
Power
Ratio*
(BPR)
Initial investment ($300 K) is included in calculations
Comparison Ratio = 3.03
Rebuild
Rebuild
Overlay
Overlay
* Buying Power Ratio = Avg. PCI Mile / $100,000 Invested

## Slide 33
PCI Points Lost per Year
Model for Pavement Life of 30 years
Pavement
Condition
Index (PCI)
Years
0
20
40
60
80
100
0
5
10
15
20
25
30
Excellent
Very Good
Fair
Failed
Good
Poor
Very Poor
Loss of 2-4 PCI Points per Year
Loss of 8-12 PCI Points per Year
Loss of 1-6 PCI Points per Year

## Slide 34
PCI Points Lost per Year
Model for Pavement Life of 30 years
Pavement
Condition
Index (PCI)
Years
0
25
40
70
85
100
0
5
10
15
20
25
30
Excellent
Very Good
Fair
Failed
Good
Poor
Very Poor
Loss of 2-4 PCI Points per Year
Loss of 8-12 PCI Points per Year
Loss of 1-6 PCI Points per Year
Waterfall
Financial liabilities
increase rapidly as the
pavement deteriorates down
the waterfall.
10
50

## Slide 35: An Analogy
Seal =
$1.50 / sq yd
Overlay =
$8 / sq yd
Reconstruct =
$30 / sq yd
repeat
slide
Process is continuous and inevitable
The rate of water flow increases as condition decreases
The effort to pump water increases with decreasing condition
Need a bigger ($) pump!

## Slide 36
( - )( )
Page 7 of 7
Costs
Efficiencies
Performance
=
Management,
PCI,
Workmanship
Remove Risks/ Hazards
Percentage %
Budget