## Slide 1: Yakima County g.r.a.s.s.
Gravel Road Aggregate Surface Stabilization
Dust Control

## Slide 2
ROAD SYSTEMS
GRAVEL | 544.59 MI.
HARD SURFACE | 1100 MI.
BRIDGES | 308
CULVERTS (36” or Bigger) | 855
RAILROAD | 22 MI.

## Slide 3: G.R.A.S.S Program
Yakima County
-Set up in 2003 w/ Reid C. Wheeler
-Criteria
- ADT
-Speed
-Res./Sense Recept.
-Traffic Safety
-Dust Sense Crops
-Crop Production Value
-Ag land Value

## Slide 4: A.D.T.

## Slide 5: Yakima Co. ADT
ADT |  | 
ADT | Miles | % of Total
0-50 | 162.26 | 29.84%
50-100 | 168.28 | 30.94%
100-200 | 159.87 | 29.40%
200-500 | 49.05 | 9.02%
500-1000 | 3.94 | 0.72%
1000-UP | 0.45 | 0.08%
ADT |  | 

## Slide 6
G_R_A_S_S
GRAVEL ROAD AGGRIGATE SURFACE STABILIZATION
    SURVEY
      EVERY 2 YRS
      LEAD TECHS IN WINTER MONTHS
      PAPER VS TECH (FIELD FORMS OR GIS ESRI )
    INPUT
      STABILIZATION PROGRAMS (SPREADSHEET)
      PRIORITY BASED ON PROGRAM
    BUDGET
      DETERMINE MILEAGE BASED ON COST
      DRAW LINE ON PRIORITY.
    WHAT MAKES SENSE
      DEAD ENDS
      ROADS WE MAY BE ABLE TO APPLY ½ RATE
      JUSTIFICATION
    ROUTE
      FIRST LAST, LAST FIRST
      MAP ROUTE

## Slide 7
MgCl2

## Slide 8
G_R_A_S_S
GRAVEL ROAD AGGRIGATE SURFACE STABILIZATION
    PREP
      ROADS HAVE BEEN SOFTEN UP AND GRADED AT LEAST 1 TIME
      DITCHING / RE-SHAPE DONE EARLY ENOUGH
      ROCK ADDED AND INCORPORATED IF NEEDED
    APPLY
      GRADERS (2)
      WATER TRUCK(s) FOR GRADERS
      DISTRIBUTOR
      WATER TRUCK FOR DISTRIBUTOR
      (2) TANKERS NURSE DISTRIBUTOR
H2O
H2O
H2O
MgCl2
MgCl2
MgCl2

## Slide 9
G_R_A_S_S
GRAVEL ROAD AGGRIGATE SURFACE STABILIZATION
    TRACK
    STATS
      AVG. PRODUCTION = 6 MILES/DAY
      PRODUCT = DUST GUARD (ROADWISE/ENVIROTECH)
      COST = $99 - $105/TON
      COST / MI = $4300
        MATERIAL = $3450 - 80%
        LABOR/EQUIP = $850 - 20%
        PROGRAM MILES 220
    ISSUES
      REDUCED BUDGET – PUBLIC EXPECTATIONS
      MATERIAL COST – ALWAYS ON RISE
      EQUIPMENT COST
      RAILROAD

## Slide 10
CURRENT YEAR |  | 
CURRENT YEAR | 2016 | 
CURRENT BUDGET | 1,100,000.00 | 
EXPECTED COST |  | % OF COST
LABOR | $118,097.07 | 10.74%
EQUIPMENT | $106,539.33 | 9.69%
MATERIALS | $855,726.05 | 77.79%
MATERIALS/FUEL | $3,660.34 | 0.33%
OTHER SERVICES | $15,977.21 | 1.45%
GROSS COST | $1,100,000.00 | 100.00%
EXPECTED MILES |  | 
RD MILES | 250.00 | 
EXPECTED COST/MI | $4,400.00 |