## Slide 1
Common Types of Chip Seal Oils
CRS-2P
CRS-3P
PMCRS-2H
HFE-100-S / HFRS-P2
HFE-90-1-S / HFRS-P1
AC-15P
HFE-150/HFMS-2
RS-LTP
CRS-LTP

## Slide 2
PMRE
CRS-2

## Slide 3
AC-15P - hot applied oil with coated aggregate
CRS-2P – Cationic rapid set emulsion with polymers
CRS-3P – Cationic rapid set emulsion with more polymers – for high traffic roads
PMCRS-2H – Cationic rapid set emulsion with polymers with harder pen oil base.
HFRS-P1- Anionic rapid set emulsion with 1.5% polymers
HFRS-P2 – Anionic rapid set emulsion with 3% polymers – for high traffic roads
RS-LTP – Anionic Low Temperature emulsion oil for use in heavy shade and along the coastal fog belt. Can be used where air temperatures are between 40 to 70 degrees
Common Chip Seal Oils

## Slide 4
CRS-LTP – Cationic low-temperature oil for use under tree canopy and coastal areas where temperatures can be between 40 and 70 degrees
HFMS 2/HFE-150 – medium set high float oil often used for gravel road conversions or with dirtier aggregate
CSS-1 – tack coat emulsion oil. Can be used as fog seal
CSS-1H – often used as a Cationic fog seal. Like CSS-1 but with a harder pen asphalt base
CQS-1H – Cationic quick set fog seal
HFRS-P1 D 50% - Anionic fog seal
Common Chip Seal Oils