## Slide 1
Curry County Chip Seal Program
2023 Chip Seal Workshop
Presented by Gary Wolford and Allan Avery

## Slide 3
Square miles: 1,648
Population: 22,915 (2021)
Road miles: 225 miles
Paved miles: 191 plus 9 miles oil mat
Road department budget: $6.0-6.5 Million
Curry County Statics

## Slide 4
Curry County Vision and Strategic Plan
Efficiency – make all maintenance programs efficient
Effectiveness – chip seals that have a 7-10-year service life
New Materials – utilize new improvements in emulsion oils
New Equipment – upgrade distributor, chip spreader and rollers
Interagency Agreements – partner with USFS and ODOT
Training – pre-season classroom and operational training

## Slide 5
Why Curry County Chip Seals
Budget shortfall of $3M to $3.5M due to loss of timber receipts
Contract 2-inch asphalt overlay about $210,000 per mile
Self-preformed chip seal about $38,000 per mile
Can chip seal 5.5 miles of road per 1 mile of overlay

## Slide 6
Curry County Climate Challenges
SW Oregon Coast two distinct climates
Coastal fog belt - average temperature about 65 degrees
Hot interior - interior valleys average about 89 degrees

## Slide 7
Cut back on overlay miles from 6 miles to 3 miles
Increased chip seal by 5 miles
Saved $500,00 per year for new equipment
Purchased new chip spreader, distributor and rollers
Equipment Purchasing Strategy

## Slide 8
Chip Spreader Upgrade

## Slide 9
Curry County Rollers

## Slide 10
South Bank Chetco River Road
Canopy
Moisture from coastal fog
Along the Chetco River
North side of mountains

## Slide 11
One year old chip seal CRS-2P chip sealed in 2017
Chip sealing with RS-LTP in 2018

## Slide 12
Aggregate loss from previous chip seal

## Slide 13
South Bank Chetco River Road in 2020

## Slide 15
Collaboration with Other Agencies
Through interagency agreements:
Curry County chip sealed 29 miles for ODOT in 2020, 2021
Curry County chip sealed 17 miles for the UFFS in 2022

## Slide 16
Pre-Season Chip Seal Training

## Slide 17
Curry County Chip Seal Crew