## Slide 1
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 2: LINN COUNTY
Approx. 1,139 total miles
Approx. 98 gravel miles
Four Maintenance Districts dividing the County into quadrants
Hilly landscapes eastern half. Flat landscapes western.
Heavy loads are mostly from logging, and hay & seed.
ALBANY
LEBANON
MILL CITY
BROWNSVILLE
SWEET HOME
TANGENT
HARRISBURG
SCIO
LYONS
HALSEY

## Slide 3
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 4: Inter-Agency Cooperation

## Slide 5: Inter-Agency Cooperation

## Slide 6
Inter-Agency Cooperation

## Slide 7: Inter-Agency Cooperation

## Slide 8
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 9: COMMUNICATION

## Slide 10: COMMUNICATION

## Slide 11: COMMUNICATION
Hearing Protection

## Slide 12: COMMUNICATION
Hearing Protection
Open Microphone
Efficiency of Operations

## Slide 13: COMMUNICATION
Hearing Protection
Open Microphone
Efficiency of Operations
Safety

## Slide 14: COMMUNICATION
Hearing Protection
Open Microphone
Efficiency of Operations
Safety
Listen-Through Capability

## Slide 15
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 16: contractors
Slurry Seals / Microsurface / MicroCoat
Fog Sealing
Crack Sealing

## Slide 17: contractors
Day 1
Chip Seal by County

## Slide 18: contractors
Day 2
Sweep & Fog Seal by Contractor

## Slide 19: contractors
Day 3
Stripe by County

## Slide 20
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 21: Paved intersections
Knox Butte Rd.

## Slide 22: Paved intersections
Harbor Rd.
Intersection
Lickskillet Rd.
Intersection
Knox Butte Rd.

## Slide 23: Paved intersections
Typical Contract
Scio District
Typical Contract
Sweet Home District

## Slide 24: Paved intersections
Add in other work
Devaney Bridge

## Slide 25: Paved intersections
Add in other work
Note: Fog seal/sand seal new asphalt before chip sealing it.
Kingston-Jordan Dr.
Pre-Level Road

## Slide 26
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 27: Single shot
Linn County:
Mostly CRS-3P or CHFRS-2P
Oil applied at 0.38 – 0.48 gals / SY
0.42 – 0.44 typical
7 – 9 miles/day, ideally
180 – 250 tons/day

## Slide 28: Single shot
3/8” – 10 oil rock
Rock applied at 17 – 20 Lbs / SY
18 pounds typical
Fog seal @ 0.12 – 0.13 gals/SY

## Slide 29: Single shot
Diamond Hil Dr. 2017
Best Practice:
Repair potholes & base failures

## Slide 30: Single shot
Kennel Road 2018
Looney Lane 2018
Best Practice:
Seal cracks
Preferably the year before chip seal is scheduled
Repair ruts

## Slide 31: Single shot
Berlin Rd. 2018
Berlin Road 2019
What if you can’t get to all the repairs or get the crack sealing done?
Chip it anyway.

## Slide 32: Single shot
Not enough oil
Cold oil
Contaminated oil or other problem
Dirty rock
Rock wasn’t rolled enough
Cold ground/air temps
Rain
Shade
Oil broke before rock cover
Etc., etc.
Shelling – Rock Loss
Repair: CRS-3P @ 0.30 gals/sy; ¼” – 10 rock @ 10 – 12 lbs/sy

## Slide 33: single shot
Oakville Rd.
South side of Hwy 34

## Slide 34: single shot
Oakville Rd.
South side of Hwy 34 - 2019
CHFRS – 2P @ 0.48 gals/SY
3/8”-10 @ 19-20 lbs/SY
Fog Seal:
BL Fog @ 0.12-0.13 gals/SY

## Slide 35
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 36: double shot
Base Course:
CRS – 3P @ 0.40 – 0.48 gals/SY; Typically 0.40 – 0.42
1/2”-1/4” @ 24-26 lbs/SY
Best practice to cure overnight before sweeping and applying the top course.
Top Course:
CRS – 3P @ 0.30 – 0.35 gals/SY
1/4” - 10 @ 13 lbs/SY
Sweep & fog seal (optional) the next day.
Fog Seal:
CQS – 1h; or QSE; or BL FOG
@ 0.10 gals/SY
Approx. 4 miles/day max. if base & top on same day.
TYPICAL SHOTS

## Slide 37: double shot
Gilkey Road 2018
PCI = 59
Gilkey Road 2019
Base Course:
CRS – 3P @ 0.46 gals/SY
1/2”-1/4” @ 24-26 lbs/SY
Top Course:
CRS – 3P @ 0.35 gals/SY
1/4” - 10 @ 13 lbs/SY
Fog Seal:
CSS – 1h @ 0.10 gals/SY

## Slide 38: double shot
Circle Dr.
2018
PCI = 14

## Slide 39: double shot
Circle Dr. 2019
Base Course:
CHFRS – 2P @ 0.48 gals/SY
1/2”-1/4” @ 24-26 lbs/SY
Top Course:
CHFRS – 2P @ 0.35 gals/SY
1/4” - 10 @ 13 lbs/SY
MicroCoat
0.35 gals/SY

## Slide 40: double shot
Circle Dr.
2019
Base Course:
CHFRS – 2P @ 0.48 gals/SY
1/2”-1/4” @ 24-26 lbs/SY
Top Course:
CHFRS – 2P @ 0.35 gals/SY
1/4” - 10 @ 13 lbs/SY
MicroCoat
0.35 gals/SY

## Slide 41: double shot
Broadway Ave.
2018
PCI = 12
No base failure

## Slide 42: double shot
Broadway Ave.
2019
Base Course:
CRS – 3P @ 0.42 gals/SY
1/2”-1/4” @ 24 lbs/SY
Top Course:
CRS – 3P @ 0.35 gals/SY
1/4” - 10 @ 12 lbs/SY
No Fog Seal

## Slide 43: double shot
Oak ST.
2018
PCI = 53
High traffic volumes: ADT 5,000+; Truck route
Base Course:
CRS – 3P @ 0.42 gals/SY
1/2”-1/4” @ 24 lbs/SY
Top Course:
CHFRS – 2P @ 0.32 gals/SY
1/4” - 10 @ 12 lbs/SY
Fog Seal: BL Fog @ 0.10 gals/SY

## Slide 44
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 45: SCRUB SEAL
The Effectiveness of the Broom on Filling the Cracks (1)
Click video image to play.

## Slide 46: SCRUB SEAL
The Effectiveness of the Broom on Filling the Cracks (2)
Click video image to play.

## Slide 47: SCRUB SEAL
Running a Wave in Front of the Broom
Click video image to play.

## Slide 48: Powerline Road
Ravelling and severe block cracking at 22174 Powerline.
Conditions Prior to Scrub Seal
Pictures taken in June of 2016.

## Slide 49: Powerline Road
Ravelling and Severe Block Cracking at 22174 Powerline.
Conditions After the Scrub Seal
Picture taken in December of 2016.

## Slide 50: Powerline Road
Ravelling and Severe Block Cracking at 22174 Powerline.
Conditions After the Scrub Seal
June of 2016.
December of 2016.

## Slide 51: Powerline Road
Ravelling and Severe Block Cracking at 22174 Powerline.
Conditions After the Scrub Seal
Picture taken 12/05/2019.
June of 2016.
December of 2016.

## Slide 52: Powerline Road
Alligator Cracking North of Lake Creek Dr.
Conditions Before the Scrub Seal
Southbound Lane
Northbound Lane
June of 2016.

## Slide 53: Powerline Road
Alligator Cracking North of Lake Creek Dr.
Conditions After the Scrub Seal
Viewing South
Viewing North
December of 2016.

## Slide 54: Powerline Road
Alligator Cracking North of Lake Creek Dr.
Conditions After the Scrub Seal
June of 2016.
December of 2016.

## Slide 55: Powerline Road
Alligator Cracking North of Lake Creek Dr.
Conditions After the Scrub Seal
June of 2016.
December of 2016.
December of 2019.

## Slide 56: Powerline Road
Alligator Cracking at Smith Seed in Halsey
Conditions After the Scrub Seal
June of 2016.
December of 2016.

## Slide 57: Powerline Road
Alligator Cracking at Smith Seed in Halsey
Conditions After the Scrub Seal
June of 2016.
December of 2016.
December of 2019.

## Slide 58: American Dr.
Picture taken at a bridge abutment, showing end of scrub seal.
Pictures taken 12/03/2019
Scrub sealed in 2017
Quarter placed on scrub seal
Quarter as shown at right

## Slide 59: American Dr.
Scrub seal

## Slide 60: Brewster rd.
When things go wrong
6.73 miles
Major collector
ADT 5,000+

## Slide 61: Brewster rd.
When things go wrong
PCI = 55 – 61
Mostly load cracking

## Slide 62: Brewster rd.
When things go wrong
Fog Seal:
CSS-1h @ 0.10 gals/sy
PASS MAX-CR (scrub seal oil – we did not use scrub broom)
0.40 gals/sy
3/8” – 10 rock @ 18-19 lbs/sy
Top Course (next day)
CRS-3P @ 0.30 gals/sy
¼” – 10 rock @ 12-13 lbs/sy

## Slide 63: Brewster rd.
When things go wrong

## Slide 64: Brewster rd.
When things go wrong

## Slide 65: Brewster rd.
When things go wrong
PASS MAX-CR has a low softening point.
Could have used less oil / more rock with the PASS in this application.
Could have used ½” rock on base course instead of 3/8”.
Could have used a harder oil on top course, not CRS-3P; or use CRS-3P on top and bottom – but not PASS combined with CRS-3P.
Could have skipped the fog seal.

## Slide 66
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 67: SAMI
Stress Absorbing Membrane Interlayer

## Slide 68: SAMI
Five Rivers Road Overlay Project
10.5 mile long project; $4.5 million
Located in Lincoln County; 25 miles east of Waldport
Managed by theFederal Highway Administration
Contract awarded to Brix Paving Northwest, Inc.
Diamond Grind existing HMAC road surface for profile and crack seal material removal.
Scrub seal performed by Sierra Santa Fe as subcontractor.
Two inch asphalt concrete overlay placed by prime contractor.
Stress Absorbing Membrane Interlayer

## Slide 69: SAMI
Helmick Road
Case Study in Polk County
This road was originally the old Highway 99. It had an 8.5” concrete base placed in 1923. The original concrete was also the wearing surface, no HMAC present. Very poor condition.
2013 – 3” HMAC overlay placed on 4 miles of roadway. After one year reflective cracking had already begun to come through the overlay.
2017 – New treatment applied to a 4 mile road segment contiguous to the above overlay. Double chip seal as SAMI: CRS-3P @ 0.42 with 3/8” - #4 @ 21 lbs. Two 1.5” lifts of HMAC placed over SAMI. HMAC dense graded mix; PG 64-22 asphalt w/ 30% RAP.
Additionally, two bridges were ground at their abutments with Geogrid installed as SAMI.
As of December 2019 no reflective cracking has appeared through the 2017 overlay.

## Slide 70
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 71: Fog Seals
Single shot chip seals:
0.11 – 0.13 gals/SY (0.12 typical)
Linn County now applies a fog seal to every single shot chip seal
Better chip retention
Better contrast for pavement markings
Double shot chip seals:
0.09 – 0.10 gals/SY (0.10 typical)
Optional but generally recommended on double shots for the above reasons
Linn County does not perform fog seals as a stand-alone treatment.

## Slide 72: Fog Seals
Double shot – No fog seal
Engel Rd.
Double shot with fog seal
Tangent Dr.
Pictures taken on same day

## Slide 73: Fog Seals
Stop using CSS-1h
Better products exist
BL Fog
QSE or
CQS-1h
CQS-1h
These products break faster; stay black longer

## Slide 74
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 75: New oil roads
Make sure you have enough good base.
This project: Arthur Dr.
16” total base section. Pothole in advance to know existing road base in multiple locations.
Digout end areas: 12” of 3”-0 with 4” of ¾” – 0 on top.
Construct in multiple well compacted lifts.
3” – 0 added to existing road base per design to achieve minimum design base thickness.
¾” – 0 placed at 4” deep, graded to shape and finished grade elevation.

## Slide 76: New oil roads
Water and roll … a lot.
The surface should be tightly graded and moist, but not wet.
Wet enough to keep the gravel base from absorbing the oil. You want the oil to stay on the surface for the oil rock to adhere.

## Slide 77: New oil roads
FIRST COURSE
¾” – ½” rock @ 52 – 55 lbs/sy
CRS-3P @ 0.50 – 0.60 gals/sy
SECOND COURSE
½” – ¼” rock @ 22 – 25 lbs/sy
CRS-3P @ 0.40 gals/sy
THIRD COURSE
¼” – 10 rock @ 12 – 14 lbs/sy

## Slide 78: New oil roads
FIRST COURSE
Don’t let the gravel road dry out in front of the chip spreader.

## Slide 79: New oil roads
Give the oil time to cure between courses.
Roll, roll, roll.

## Slide 80
Kevin Hamilton
Construction & Rd. Maint. Sup.
(541) 967-3919 Office
(541) 740-1787 Cell
khamilton@co.linn.or.us
Jeff Maskal
Maintenance Worker III
Leadworker for Chip Seal Operations
(541) 967-3919 Office/Message
Surface treatment toolbox
in Linn County, OR
Inter-Agency Cooperation
Communication
Contract Work
Paved Intersections
Single Shot Chip Seals
Double Shot Chip Seals
Scrub Seals
SAMI
Fog Seals
New Oil Mat Roads
Combatting Flushing/Bleeding Roads

## Slide 81
FIRST COURSE
¾” – ½” rock
@ 52 – 55 lbs/sy
CRS-3P
@ 0.46 gals/sy
SECOND COURSE
3/8” – 10 rock
@ 18 – 22 lbs/sy
CRS-3P
@ 0.38 gals/sy
Flushing/bleeding roads
Langmack Rd.
May of 2018.

## Slide 82
FIRST COURSE
¾” – ½” rock
@ 52 – 55 lbs/sy
CRS-3P
@ 0.46 gals/sy
SECOND COURSE
3/8” – 10 rock
@ 18 – 22 lbs/sy
CRS-3P
@ 0.38 gals/sy
Flushing/bleeding roads
Langmack Rd.
December of 2019.

## Slide 83
FIRST COURSE
¾” – ½” rock
@ 52 – 55 lbs/sy
CRS-3P
@ 0.46 gals/sy
SECOND COURSE
3/8” – 10 rock
@ 18 – 22 lbs/sy
CRS-3P
@ 0.38 gals/sy
No fog seal
Flushing/bleeding roads
Langmack Rd.
December of 2019.

## Slide 84
Three courses of rock.
Two courses of oil.
No fog seal
Flushing/bleeding roads
Parker Rd.
2011
SANDWICH SEAL

## Slide 85
FIRST COURSE
½” – ¼” rock @ 20 – 24 lbs/sy
No oil.
Roll, roll, roll.
SECOND COURSE
Applied CRS-2P @ 0.35 gals/sy,
Then ½” – ¼” rock @ 22 - 24 lbs/sy again.
Roll, roll, roll. Then sweep.
THIRD COURSE
Applied CRS-2P @ 0.40 gals/sy
Then ¼” – 10 rock @ 18 – 20 lbs/sy.
Roll.
Flushing/bleeding roads
Parker Rd.
2011
SANDWICH SEAL

## Slide 86
FIRST COURSE
½” – ¼” rock @ 20 – 24 lbs/sy
No oil.
Roll, roll, roll.
SECOND COURSE
Applied CRS-2P @ 0.35 gals/sy,
Then ½” – ¼” rock @ 22 - 24 lbs/sy again.
Roll, roll, roll. Then sweep.
THIRD COURSE
Applied CRS-2P @ 0.40 gals/sy
Then ¼” – 10 rock @ 18 – 20 lbs/sy.
Roll.
Flushing/bleeding roads
Parker Rd.
After sandwich seal in 2011
SANDWICH SEAL

## Slide 87
Flushing/bleeding roads
Parker Rd.
After sandwich seal in 2011
SANDWICH SEAL
Parker Rd.
July, 2018